## Slide 1: ALFRED: Bump and Wander Design
Helen_controller
Cmd_velocity_msg
NOTES:
This is the simplest implementation of the Glow Worm system I’ve put together as a demonstration of how to build a publish and subscribe architecture with an open loop system.
Bumper_plant
Two_bumper_msg
gw::Bumper* x2
Rover_plant
gw::Motor* 2
Helen_bot.ino

## Slide 2: ALFRED: Bump and Wander with Light Plant
Helen_controller
Cmd_led_msg
Cmd_velocity_msg
NOTES:
The addition of the light plant requires the Helen_controller to publish two messages.
The light plant also uses the I2C digital I/O expander and requires the Wire library which is a memory hog.
Bumper_plant
Two_bumper_msg
gw::Bumper* x2
Rover_plant
gw::Motor* 2
Light_plant
gw::Led* 5
Helen_bot.ino

## Slide 3: ALFRED: Scan and Wander
Whisker_controller
Cmd_velocity_msg
NOTES:
This bot implements obstacle avoidance by rotating an ultrasonic sensor with an attached servo.
The Scanner_5pt block hides the implementation and control details for controlling the scan.
Scanner_5pt
Five_pt_scan_msg
Servo.h x2
Parallax PING))) x 1
Rover_plant
gw::Motor* 2
Whisker_bot.ino

## Slide 4: ALFRED: Scan and Wander with Lights
NOTES:
This bot implements obstacle avoidance by rotating an ultrasonic sensor with an attached servo.
This version adds the light plant to give a visual indication of which “whisker” was tripped by an obstacle.
Scanner_5pt
Five_pt_scan_msg
Servo.h x2
Parallax PING))) x 1
Rover_plant
gw::Motor* 2
Light_whisker_bot.ino
Whisker_controller
Cmd_led_msg
Cmd_velocity_msg
Light_plant
gw::Led* 5

## Slide 5: ALFRED: Scan, Bump and Wander with Lights
NOTES:
This bot implements obstacle avoidance by rotating an ultrasonic sensor with an attached servo.
This version adds the light plant to give a visual indication of which “whisker” was tripped by an obstacle.
Scanner_5pt
Five_pt_scan_msg
Servo.h x2
Parallax PING))) x 1
Rover_plant
gw::Motor* 2
SBW_bot.ino
Whisker_controller
Cmd_led_msg
Cmd_velocity_msg
Light_plant
gw::Led* 5
Bumper_plant
Two_bumper_msg
gw::Bumper* x2